## Slide 1: Encoding ECMP/UCMP information in PCEP
M. Koldychev – Cisco Systems (mkoldych@cisco.com) – Presenter
M. Sivabalan – Cisco Systems (msiva@cisco.com)
D. Dhody – Huawei Technologies (dhruv.ietf@gmail.com)
IETF 105 – Montreal PCE Working Group

## Slide 2: Encoding ECMP/UCMP information in PCEP
We are motivated by the need to encode multiple Segment Lists in SR-TE Policies, but our results are meant to be generic.
Terminology:
ERO == Explicit Route Object
LSP == PCEP LSP (identified by LSP-IDENTIFIERS)

## Slide 3: Motivation
In SR-TE Policy, the optimization problem is defined by optimization objectives and constraints and the solution to the optimization problem is a set of Segment Lists.
https://tools.ietf.org/html/draft-ietf-spring-segment-routing-policy-03
A dynamic candidate path expresses an optimization objective and a
set of constraints. The headend (potentially with the help of a PCE)
computes the solution Segment-List (or set of Segment-Lists) that
solves the optimization problem.
If a candidate path is associated with a set of Segment-Lists, each
Segment-List is associated with a weight for weighted load balancing
(refer Section 2.11 for details). The default weight is 1.

## Slide 4: Motivation (cont’d)
Two use-cases:
One optimization objective yields multiple ECMP paths.
Multiple optimization objectives sharing ECMP.
These two use-cases are orthogonal, they exist independently of each other.
For example:
LSP 1 and LSP 2 have different optimization objectives and ECMP is desired
LSP 1 gets a single path X
LSP 2 gets two ECMP paths: Y and Z
As a result 50% of traffic goes on path X, 25% on path Y and 25% on path Z.

## Slide 5: Use Case 1
Use Case 1: single optimization objective yields multiple paths.
Extend PCEP to specify the maximum number of ECMP paths that the PCC can handle
Extend PCEP to allow for multiple ERO objects within a single LSP, some options are possible:
  define a new object to “separate” the EROs and carry per-ERO attributes
  follow RFC 8623 for encoding multiple EROs
  other proposals (to be discussed on mailing list)

## Slide 6: Analysis of Option A
We can replace a single ERO object by multiple ERO objects, separated by a new ERO-ATTRIBUTES object.
Current BNF:
<intended-path> = <ERO>
Proposed BNF: <intended-path> = <ero-list>
<ero-list> = [<ERO-ATTRIBUTES>]<ERO>[<ero-list>]

## Slide 7: Analysis of Option A (cont’d)
Define ERO-ATTRIBUTES object to carry some per-ERO attributes:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flags | Oper|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Weight |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Optional TLVs ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Support for ERO-ATTRIBUTES can be negotiated in the OPEN message, thus guaranteeing backward compatibility.

## Slide 8: Analysis of Option B
https://tools.ietf.org/html/rfc8623 - Stateful Path Computation Element (PCE) Protocol Extensions for Usage with Point-to-Multipoint TE Label Switched Paths (LSPs)
RFC 8623 already defines a way to carry multiple ERO/RRO objects, by using a special type of END-POINTS object and an S2LS object. We can define a new END-POINTS and S2LS object types for P2P load-balancing and then we can follow the same encoding format as RFC 8623.

## Slide 9: Analysis of Option B (cont’d)
S2LS format is almost the same as ERO-ATTRIBUTES, except that it’s missing the Weight field:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flags | Oper|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Optional TLVs ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
The weight can be either carried in an optional TLV, or it can be embedded directly as part of the new S2LS object type.
New END-POINTS object type would need to be defined, to specify that the S2LS objects that follow it are for ECMP/UCMP.

## Slide 10: Analysis of Option B (cont’d)
For example, suppose the PCE was computing a path from Source A to Destination X and the result was 2 EROs: {A,B,X} and {A,C,X}. Suppose that the 2 EROs have UCMP weights 2 and 3 respectively. Then the PCE would encode this as follows:
Common Header
LSP
END-POINTS (SRC=A, DEST=X)
S2LS (O=UP, WEIGHT=2)
ERO1={A,B,X}
END-POINTS (SRC=A, DEST=X)
S2LS (O=UP, WEIGHT=3)
ERO2={A,C,X}
Note that we need to encode 2 END-POINTS objects here if we want to encode 2 S2LS objects, in order to conform to the RBNF of RFC 8623. If both EROs had the same weight (ECMP), then we would not need 2 S2LS objects and we would encode ERO2 directly after ERO1.

## Slide 11: Use Case 2
Use Case 2: multiple optimization objectives sharing ECMP.
Allocate a different PCEP Tunnel for every objective.
Create a new PCEP association type (Ex., “ECMP Association”) to bind these Tunnels together.

## Slide 12: Combination of both Use Cases
Going back to our previous example:
LSP 1 and LSP 2 have different optimization objectives and ECMP is desired
LSP 1 gets a single path X
LSP 2 gets two ECMP paths: Y and Z
As a result 50% of traffic goes on path X, 25% on path Y and 25% on path Z.
PCEP representation of the above:
ECMP ASSOCIATION contains LSP 1 and LSP 2.
LSP 1 contains a single ERO: X.
LSP 2 contains two EROs: Y and X.