## Slide 1: Encoding multipath information in PCEP
Motivated by the need to encode multiple Segment Lists in SR-TE Policies, but results are applied to RSVP-TE as well.
Terminology:
ERO == Explicit Route Object
LSP == PCEP LSP (identified by LSP-IDENTIFIERS TLV)

## Slide 2: Motivation
We want the PCE to be able to install not just a single path, but multiple ECMP/UCMP paths from source to destination.
https://tools.ietf.org/html/draft-ietf-spring-segment-routing-policy-03
A dynamic candidate path expresses an optimization objective and a
set of constraints. The headend (potentially with the help of a PCE)
computes the solution Segment-List (or set of Segment-Lists) that
solves the optimization problem.
If a candidate path is associated with a set of Segment-Lists, each
Segment-List is associated with a weight for weighted load balancing
(refer Section 2.11 for details). The default weight is 1.

## Slide 3: LSP objectives and constraints
The PCE runs a computation algorithm that takes objectives and constraints as the input and produces a set of EROs as the output. PROBLEM TO SOLVE: PCEP lacks a way to signal multiple EROs to the head-end.
SR Policies statically configured on the PCC may have more than one Segment List in a Candidate Path. PROBLEM TO SOLVE: PCEP lacks a way to signal multiple Segment Lists to the PCE.

## Slide 4: Proposed solutions
Solution 1: allocate a different LSP for every ERO and create a new association type to bind these LSPs together.
Solution 2: one LSP contains many EROs.
Option 2a: define a new object for ERO attributes.
Option 2b: follow RFC 8623 for encoding multiple EROs.
.

## Slide 5: Analysis of Solution 1
Solution 1: allocate a different LSP for every ERO and create a new association type to bind these LSPs together.
May work for PCE-initiated LSPs, because the PCE knows how many EROs it computed and can instantiate that many LSPs.
Does not work for PCC-initiated LSPs, because the PCC would need to know how many EROs the PCE will compute and delegate that many LSPs.
Opens the possibility of each ERO in the set having different objectives and constraints, which is inconsistent.
Does not allow all the EROs to be reported/updated/instantiated together, since each LSP is reported/updated/instantiated separately from the others.

## Slide 6: Analysis of Solution 2a
Solution 2: one LSP contains many EROs.
Option 2a: define a new object for ERO attributes
We can replace a single ERO object by multiple ERO objects, separated by a new ERO-ATTRIBUTES object.
Current BNF:
<intended-path> = <ERO>
Proposed BNF: <intended-path> = <ero-list>
<ero-list> = [<ERO-ATTRIBUTES>]<ERO>[<ero-list>]

## Slide 7: Analysis of Solution 2a (cont’d)
Define ERO-ATTRIBUTES object to carry some per-ERO attributes:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flags | Oper|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Weight |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Optional TLVs ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Support for ERO-ATTRIBUTES can be negotiated in the OPEN message, thus guaranteeing backward compatibility.

## Slide 8: Analysis of Solution 2b
Solution 2: one LSP contains many EROs.
Option 2b: follow RFC 8623 for encoding multiple EROs.
https://tools.ietf.org/html/rfc8623 - Stateful Path Computation Element (PCE) Protocol Extensions for Usage with Point-to-Multipoint TE Label Switched Paths (LSPs)
RFC 8623 already defines a way to carry multiple ERO/RRO objects, by using a special type of END-POINTS object and an S2LS object. We can define a new END-POINTS and S2LS object types for P2P load-balancing and then we can follow the same encoding format as RFC 8623.

## Slide 9: Analysis of Solution 2b (cont’d)
S2LS format is almost the same as ERO-ATTRIBUTES, except that it’s missing the Weight field:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flags | Oper|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Optional TLVs ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
The weight can be either carried in an optional TLV, or it can be embedded directly as part of the new S2LS object type.
New END-POINTS object type would need to be defined, to specify that the S2LS objects that follow it are for ECMP/UCMP.

## Slide 10: Analysis of Solution 2b (cont’d)
For example, suppose the PCE was computing a path from Source A to Destination X and the result was 2 EROs: {A,B,X} and {A,C,X}. Suppose that the 2 EROs have UCMP weights 2 and 3 respectively. Then the PCE would encode this as follows:
Common Header
LSP
END-POINTS (SRC=A, DEST=X)
S2LS (O=UP, WEIGHT=2)
ERO1={A,B,X}
END-POINTS (SRC=A, DEST=X)
S2LS (O=UP, WEIGHT=3)
ERO2={A,C,X}
Note that we need to encode 2 END-POINTS objects here if we want to encode 2 S2LS objects, in order to conform to the RBNF of RFC 8623. If both EROs had the same weight (ECMP), then we would not need 2 S2LS objects and we would encode ERO2 directly after ERO1.

## Slide 11: Comparison of solutions
Solution 1: allocate a different LSP for every ERO and create a new association type to bind these LSPs together.
  Multiple problems with this, would not really fit into the database structure
Solution 2: one LSP contains many EROs.
Option 2a: define a new object for ERO attributes
    Separate RBNFs for P2P and P2MP
Option 2b: follow RFC 8623 for encoding multiple EROs.
    Common RBNF for P2P and P2MP