## Slide 1: Encoding ECMP/UCMP information in PCEP
IETF 105 – Montreal PCE Working Group

## Slide 2: Encoding ECMP/UCMP information in PCEP
We are motivated by the need to encode multiple Segment Lists in SR-TE Policies, but our results are meant to be generic.
Terminology:
ERO == Explicit Route Object
LSP == PCEP LSP (identified by LSP-IDENTIFIERS)

## Slide 3: Motivation
In SR-TE Policy, the optimization problem is defined by optimization objectives and constraints and the solution to the optimization problem is a set of Segment Lists.
https://tools.ietf.org/html/draft-ietf-spring-segment-routing-policy-03
A dynamic candidate path expresses an optimization objective and a
set of constraints. The headend (potentially with the help of a PCE)
computes the solution Segment-List (or set of Segment-Lists) that
solves the optimization problem.
If a candidate path is associated with a set of Segment-Lists, each
Segment-List is associated with a weight for weighted load balancing
(refer Section 2.11 for details). The default weight is 1.

## Slide 4: Motivation (cont’d)
In SR-TE, the computed set of Segment Lists is installed in a single update, not in incremental updates.
In SR-TE, there is no use case for ECMP among paths with different optimization objectives.
  “A dynamic candidate path expresses an optimization objective and a set of constraints.”
  Only one candidate path can be active at any given time.

## Slide 5: Proposed solutions
Solution 1: allocate a different LSP for every ERO and create a new association type to bind these LSPs together.
Solution 2: one LSP contains many EROs.
Option 2a: define a new object to carry ERO attributes.
Option 2b: follow RFC 8623 for encoding multiple EROs.

## Slide 6: Analysis of Solution 1
Solution 1: allocate a different LSP for every ERO and create a new association type to bind these LSPs together.
Does not work for PCC-initiated, because the PCC would need to know how many EROs the PCE will compute and delegate that many LSPs.
Does not allow all the EROs to be reported/updated/instantiated together, since each LSP is reported/updated/instantiated separately from the others.
Better used for signaling ECMP among paths with different objectives, because each LSP encodes a separate objective.

## Slide 7: Analysis of Solution 1 (cont’d)
Doing ECMP among paths with different objectives is orthogonal to doing ECMP among paths with a single objective. Both situations can exist at the same time.
For example LSP 1 and LSP 2, having different objectives, can have ECMP among each other using solution 1. While, LSP 1 itself has multiple ECMP paths within it.
ECMP among paths with different objectives is not applicable SR-TE.

## Slide 8: Analysis of Solution 2a
Solution 2: one LSP contains many EROs.
Option 2a: define a new object to carry ERO attributes
We can replace a single ERO object by multiple ERO objects, separated by a new ERO-ATTRIBUTES object.
Current BNF:
<intended-path> = <ERO>
Proposed BNF: <intended-path> = <ero-list>
<ero-list> = [<ERO-ATTRIBUTES>]<ERO>[<ero-list>]

## Slide 9: Analysis of Solution 2a (cont’d)
Define ERO-ATTRIBUTES object to carry some per-ERO attributes:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flags | Oper|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Weight |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Optional TLVs ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Support for ERO-ATTRIBUTES can be negotiated in the OPEN message, thus guaranteeing backward compatibility.

## Slide 10: Analysis of Solution 2b
Solution 2: one LSP contains many EROs.
Option 2b: follow RFC 8623 for encoding multiple EROs.
https://tools.ietf.org/html/rfc8623 - Stateful Path Computation Element (PCE) Protocol Extensions for Usage with Point-to-Multipoint TE Label Switched Paths (LSPs)
RFC 8623 already defines a way to carry multiple ERO/RRO objects, by using a special type of END-POINTS object and an S2LS object. We can define a new END-POINTS and S2LS object types for P2P load-balancing and then we can follow the same encoding format as RFC 8623.

## Slide 11: Analysis of Solution 2b (cont’d)
S2LS format is almost the same as ERO-ATTRIBUTES, except that it’s missing the Weight field:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Flags | Oper|
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
~ Optional TLVs ~
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
The weight can be either carried in an optional TLV, or it can be embedded directly as part of the new S2LS object type.
New END-POINTS object type would need to be defined, to specify that the S2LS objects that follow it are for ECMP/UCMP.

## Slide 12: Analysis of Solution 2b (cont’d)
For example, suppose the PCE was computing a path from Source A to Destination X and the result was 2 EROs: {A,B,X} and {A,C,X}. Suppose that the 2 EROs have UCMP weights 2 and 3 respectively. Then the PCE would encode this as follows:
Common Header
LSP
END-POINTS (SRC=A, DEST=X)
S2LS (O=UP, WEIGHT=2)
ERO1={A,B,X}
END-POINTS (SRC=A, DEST=X)
S2LS (O=UP, WEIGHT=3)
ERO2={A,C,X}
Note that we need to encode 2 END-POINTS objects here if we want to encode 2 S2LS objects, in order to conform to the RBNF of RFC 8623. If both EROs had the same weight (ECMP), then we would not need 2 S2LS objects and we would encode ERO2 directly after ERO1.

## Slide 13: Comparison of solutions
Solution 1: allocate a different LSP for every ERO and create a new association type to bind these LSPs together.
  Works for paths with different objectives
  Does not work for paths with the same objective
Solution 2: one LSP contains many EROs.
Option 2a: define a new object for ERO attributes
    Separate RBNFs for P2P and P2MP
Option 2b: follow RFC 8623 for encoding multiple EROs.
    Common RBNF for P2P and P2MP
    Need to insert “extra” objects, like END-POINTS